## Slide 1: Point-to-point protocol exploration
Nayib Boukadida
n.boukadida@nikhef.nl
F. Schreuder
A. Borga
P. Jansweijer
W.E. Dolman

## Slide 2: Content
About Nikhef
Internship assignment
Structure of communication protocols
Requirements
Survey of existing protocols (vendor dependent and independent)
The Interlaken protocol
Implementation
Status
Conclusion

## Slide 3: Nikhef
National Institute for Subatomic Physics (Nationaal Instituut voor Subatomaire fysica)
Among others, Nikhef is closely involved in the development of the LHC ATLAS experiment at CERN
Internship at the Electronic Technology department

## Slide 4: Internship assignment
Large particle detector facilities often require a point-to-point link at a certain stage of the DataAcQuisition (DAQ) chain to connect custom tailored electronics
As the demand of data processing increases and larger data-sets are to be transported through these links their performance in terms of speed and bandwidth must scale accordingly
Because of this:
I was assigned the task to research and implement a novel high-speed point-to-point link targeting FPGA communication

## Slide 5: Internship assignment
Explore how point-to-point communication protocols are built up
Survey the currently existing point-to-point protocols
Find out if there is an existing protocol that matches a set of clear requirements
Describe the protocol and implement a proof of concept that can run on an FPGA [possibly vendor independent]
Publish specifications and implementation as Free and Open Source on specialized code hosting platforms like OpenCores
sharing is done with the aim of promoting the dissemination and broad adoption of the design
Notes: I was asked to…

## Slide 6: Point-to-point protocols
Open Systems Interconnection (OSI) model
Describes how data communication between two peers should take place
Focused on FPGA
The media layer will be of most interest to us
  Layer 1 : Physical (PHY)
  Layer 2 : Data link (MAC)

## Slide 7: Point-to-point protocols
Data structure and framing (OSI Layer 2)
    Adds overhead for the peers to properly handle payload data
Error detection and correction (OSI Layer 2/1)
    Checks on erroneous/flipped bits
Encoding of data (OSI Layer 1)
    Ensures the data will arrive “electrically” correct
Serialization and deserialization of data (OSI Layer 1)
    Long distance communication happens over serial link [stating the obvious]

## Slide 8: Line encoding and decoding
Encoding adds sync headers and randomizes the binary data
  Prevents baseline wander, constant EMI
  Prevents errors in delineation of words
  Essential for clock recovery
Scrambler
  Randomizes the data according to an algorithm
  Can be reversed by the receiver [this is not encryption]
  Prevents long rows of continuous binary values
  Can be self-synchronous (on payload) or independent synchronous (per lane)
Commonly used:
8b/10b - DVI / HDMI / Gbit Eth SGMI / SATA / USB 3.0
64b/66b - Ethernet / InfiniBand / Thunderbolt
128b/130b - PCIe 3.0/4.0
128b/132b - USB 3.1
256b/257b - Fibrechannel
64b/67b - Interlaken

## Slide 9: Flow control and bonding
Flow control
  Start/stop transmitting at command of the receiver
  Prevents overwhelming the receiver
Channel Bonding
  Combining multiple serial links in parallel
  Increases throughput

## Slide 10: Requirements
Mandatory:
  Line rate must be at least 10 Gbit/s (1,25 GB/s)
  Flow control must be present
  Range distance coverage has to be 10 - 200 meters (normal distance)
Optional:
  Cyclic Redundancy Check
  Forward Error Correction
  Channel bonding

## Slide 11: Survey
Vendor dependent protocols
Altera SerialLite II & III
  Speeds up to 28 Gbit/s (Transceiver dependent)
  SLII supports flow control / SLIII not very clear
  CRC-32 Error Correction
  FEC not mentioned
  64b/67b encoding
Xilinx Aurora 8b/10b & 64b/66b
  Speeds up to 26 Gbit/s (Transceiver dependent)
  Flow control
  CRC-32 Error correction
  FEC not mentioned
  64b/66b encoding
Microsemi litefast – Somewhat older

## Slide 12: Survey
Vendor independent protocols
Interlaken
  Clear documentation
  meets all requirements by a fair margin
SATA
  Lane rate is not sufficient
  Older 8b/10b encoding
  Includes flow control / CRC-32
  Not open source
  No bonding
CPRI
  Unclear documentation
  Sufficient lane rate and encoding
  Channel bonding not supported
HyperTransport
  High speeds
  Parallel bus
Fibre Channel
  No documentation found
  Only old presentations to be found
  Not open
XAUI
  Combines multiple slower line to 10 Gbps link
  Used in combination with Ethernet
This slide is explicitly full of stuff! 

## Slide 13: Survey
Vendor independent protocols
Interlaken
  Clear documentation
  meets all requirements by a fair margin
SATA
  Lane rate is not sufficient
  Older 8b/10b encoding
  Includes flow control / CRC-32
  Not open source
  No bonding
CPRI
  Unclear documentation
  Sufficient lane rate and encoding
  Channel bonding not supported
HyperTransport
  High speeds
  Parallel bus
Fibre Channel
  No documentation found
  Only old presentations to be found
  Not open
XAUI
  Combines multiple slower line to 10 Gbps link
  Used in combination with Ethernet
This slide is explicitly full of stuff! 

## Slide 14: The Interlaken Protocol
Revision 1.2 October 7, 2008
Property of Cortina Systems and Cisco Systems
Royalty-free
Interlaken Alliance
Many members, among others:
    Broadcom, Intel, Lattice, Microsemi, Xilinx
It was made because…

## Slide 15: Implementation
Worked on a implementation in VHDL – target Xilinx VC707 board
Only the transceiver and FIFOs make use of a proprietary IP Core
Overhead (Single lane)
    Bursts : BurstMax 32 (256 B), BurstMin 4 (32 B) -> 2/34 = 5,88% (Best case)
    Metaframing : Metaframelength 2048 (16.384 B) -> 4/2048 = 0,20%
    Encoding : 64b/67b -> 64/67 = 4,48%
    Total overhead of about 10,3%
We called it Core1990

## Slide 16: Status
Found a protocol that meets all requirements
Described the protocol extensively in a structured document
Vivado project is properly setup and design is synthesizable
Design functions verified in behavioral simulation
  Complete transmitter and receiver chains
  CRC-24 and receiving FIFO need some adjustments
Not yet tested in hardware

## Slide 17: Conclusion
Gained knowledge
  Much more experience in writing correct VHDL
  Better idea of how to analyze IP Core documentation
  More confident in designing according to specs
  Navigate through a lot of signals in simulation
  How to properly gather and research information
  How to properly structure a specification document
My accomplishment is the first step
  Others can learn from it and continue its development
Information and documentation will be uploaded to:
https://opencores.org/project/core1990_interlaken

## Slide 18: Conclusion
Gained knowledge
  Much more experience in writing correct VHDL
  Better idea of how to analyze IP Core documentation
  More confident in designing according to specs
  Navigate through a lot of signals in simulation
  How to properly gather and research information
  How to properly structure a specification document
My accomplishment is the first step
  Others can learn from it and continue its development
Information and documentation will be uploaded to:
https://opencores.org/project/core1990_interlaken
Thank you for your attention! 

## Slide 19: Backup slides

## Slide 20: The Interlaken Protocol
Idle/burst and framing control words
Burst framing
  Covered by CRC-24
  Contains start and end
  BurstMax
  BurstMin
Burst example
Optional scheduling
  In-band flow control
  Channel numbers
This slide is a cheat sheet! 

## Slide 21: The Interlaken Protocol
Meta framing
- Covered by CRC-32
- Synchronizes the connection
- Communicates scrambler states
- Skip words for clock synchronization
- Diagnostic information
Synchronization / Scrambler state
Diagnostic word
Skip word
This slide is also a cheat sheet! 

## Slide 22: The Interlaken Protocol
CRC-32 - Meta framing
X32+X28+X27+X26+X25+X23+X22+X20+X19+X18+
X14+X13+X11+X10+X9+X8+X6+1
CRC-24 - Burst framing
X24+X21+X20+X17+X15+X11+X9+X8+X6+X5+X+1
CRC-4 - Out-of-band flow control
X4+X+1
Flow Control
- XON/XOFF
In-band flow control
- Included in burst control words
- Intended for duplex operation
Out-of-band flow control
- Covered by CRC-4
- Intended for simplex operation
This slide is also a cheat sheet! 

## Slide 23: The Interlaken Protocol
Scrambler
- Independent synchronous scrambler
- 58 bit polynomial : X58+X38+1
- No error multiplication through
multiple frames
- In case of error, synchronizes itself
Encoder
- Adds a 3-bit preamble
- 50% of combinations possible
- Running disparity within 96-bit
boundary
- Doesn’t rely on the scrambler
- Lower Bit-Error-Rate
This slide is also a cheat sheet! 